## Slide 2: MBAS841 Operations Management Analyzing Process Data
Master of Management Analytics– Session 4
Geoff Pond
Notes: An example of a title page with more specific program details in the title

## Slide 3: Process Analysis from a Managerial Perspective
We should work on our process, not the outcome of our processes.
The role of management is to change the process rather than badgering individuals to do better.

## Slide 4: Agenda
At the process design stage,
Is the process capable of meeting consumer specifications with reasonable consistency?
Following implementation,
Is the process behaving the way we expect it to?
Today, our focus will be on the collection and analysis of data to objectively answer each of the above questions.

## Slide 5: Process Capability Analysis

## Slide 6: Is my process “capable”?
Chart: 
For a process having normally distributed natural variability (many in manufacturing and production), the distribution generally appears as illustrated at left.
Recalling the empirical rule, 99.7% of a normally distributed RV falls within three standard deviations of the mean.
If 99.7% (or more) of output falls within customer specifications, the process is deemed “capable”. Tighter specifications are also very common.

## Slide 7: Is my process capable?
We use a capability index () the degree to which the process output falls within specifications:
In order to be deemed “capable”, a minimum value of must be obtained.

## Slide 8: Process Capability Analysis
Seems like a pretty simple equation. Specification limits are normally dictated to us by a customer. That leaves only the natural variability of the process ().
Critically, must represent only common variability (e.g., noise). There should be no assignable cause to the variability.

## Slide 9: Process Capability Analysis
How do I handle product specifications that are not symmetric, e.g.,
Ø2.000
+0.010
-0.005

## Slide 10: Six-Sigma Process Control

## Slide 11: Process Control
Defect Rates
A common metric in quality circles is the number of Defects Per Million Opportunities (DPMO) and is defined algebraically as:

## Slide 12: Process Control
At left is a very traditional graphical depiction of 6 quality management.
If we were to go to Excel and type:
=2*NORM.DIST(-6,0,1,TRUE)*1,000,000,000
=2*NORM.S.DIST(-6,TRUE)*1,000,000,000
we would get an expected 2 defects per BILLION opportunities.
But contemporary literature in 6 consistently references a DPMO of 3.4. This seems like a bit of a contradiction…
Chart: 
UTL

## Slide 13: Process Control
Chart: 
UTL
Process capability studies are largely founded in the work done by Motorola in the 1980s and 1990s. Motorola found that processes naturally drift over time. They may drift in one direction naturally and as time continues, start to drift back – without any intervention whatsoever.
Motorola termed this the “Long Term Dynamic Mean Variation” and found that, numerically, it resulted in a shift of 1.4 to 1.6 standard deviations from the process centre.
This has since become known as the “1.5 sigma shift”.

## Slide 14: Process Control
Graphically, this is represented by the image at left where the process centre drifts away from the desired centre by as much as 1.5 before spontaneously starting to drift back the other way. If we considered a process that drifted as far to the right as 1.5 to the right from the mean, in Excel, we would calculate:
=NORM.DIST(-6, 1.5, 1, TRUE)*1,000,000 +
(1-NORM.DIST(6, 1.5, 1, TRUE))*1,000,000
And obtain a DPMO of approximately 3.4 (just like the quality literature suggests we should)
Chart: 
UTL

## Slide 15: Process Control
That’s a really nice picture but what makes me think that things are normally distributed?
Central Limit Theorem
It doesn’t matter what the distribution of is, the distribution of tends towards normality

## Slide 16: Process Control
Consider an exponential distribution with a mean of 80. In Excel, I generated 1,000 random numbers from such a distribution to obtain the following histogram:
Then I generated 500 random samples of 5 observations from the distribution at left. For each sample, I find the average. Then I obtained a histogram of those averages. It is approaching a normal distribution.

## Slide 17: Process Control
Chart: 
| 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | More
Sample Means | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 2 | 2 | 10 | 25 | 26 | 68 | 100 | 89 | 79 | 40 | 37 | 13 | 7 | 2 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Population | 0 | 0 | 0 | 0 | 2 | 2 | 4 | 20 | 9 | 16 | 28 | 30 | 37 | 47 | 74 | 64 | 71 | 79 | 80 | 72 | 68 | 82 | 63 | 35 | 40 | 28 | 24 | 10 | 4 | 3 | 2 | 3 | 1 | 0 | 0 | 1 | 1 | 0 | 0
Excel Experiment
1,000 individual measures
500 random samples
Does ?

## Slide 18: Process Control
No! But a relationship exists between the two:

## Slide 19: Process Control – Approximating
In reality, we seldom know so we need some other method of approximating it based on the information we have.

## Slide 20: Process Control – Approximating
Finally, combining our two previous equations,

## Slide 21: Process Control – Shehwart’s -chart
Assuming normal variability, typical practice is to set control limits to be within 3 standard deviations of the mean, so .
Chart: 

## Slide 22: Process Control – Shehwart’s -chart
Assuming normal variability, typical practice is to set control limits to be within 3 standard deviations of the mean, so .
Chart: 

## Slide 23: Process Control – Shewhart’s -chart
When we use only sample averages, we lose information related to the variability within a sample. Instead, we’re considering only the variability between samples. Recognizing this, Shewhart also introduced recommended limits on the sample range ():

## Slide 24: Process Control - Control Chart Constants
2 | 0 | 3.27 | 1.128 | 0.853
3 | 0 | 2.57 | 1.693 | 0.888
4 | 0 | 2.28 | 2.059 | 0.880
5 | 0 | 2.11 | 2.326 | 0.864
6 | 0 | 2.00 | 2.534 | 0.848
7 | 0.08 | 1.92 | 2.704 | 0.833
8 | 0.14 | 1.86 | 2.847 | 0.820
9 | 0.18 | 1.82 | 2.970 | 0.808
10 | 0.22 | 1.78 | 3.078 | 0.797
2 | 0 | 3.27 | 1.128 | 0.853
3 | 0 | 2.57 | 1.693 | 0.888
4 | 0 | 2.28 | 2.059 | 0.880
5 | 0 | 2.11 | 2.326 | 0.864
6 | 0 | 2.00 | 2.534 | 0.848
7 | 0.08 | 1.92 | 2.704 | 0.833
8 | 0.14 | 1.86 | 2.847 | 0.820
9 | 0.18 | 1.82 | 2.970 | 0.808
10 | 0.22 | 1.78 | 3.078 | 0.797

## Slide 25: Process Control – Control Charts
Chart: 
 | 3.331 | 2.8675 | 3.0528 | 2.7208 | 2.9288 | 3.039 | 3.7414 | 2.8014 | 3.1462 | 2.3285 | 3.463 | 2.9655 | 3.8099 | 2.3611 | 3.5361 | 3.1912
 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2 | 2.2
 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8 | 3.8
 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3 | 3
UCL
LCL
mean
Sample Number
Sheet Thickness (mm)
Note: This is the average within a sample

## Slide 26: Process Control – Control Charts

## Slide 27: Process Control – Control Charts

## Slide 28: Statistical Process Controls
What it is NOT:
a tool to determine whether a lot of goods is within specification
  This is called “acceptance sampling” and is something altogether different
What it IS:
a tool to identify when our process is behaving in an unexpected way
we use product/service measures in order to better understand the behaviour of the process that fabricated/delivered those products/services
when the process is behaving unexpectedly, as demonstrated by our control measures, this is a signal to management to intervene

## Slide 29: Break Time

## Slide 30: Control Charts – Unbiased or biased?
Shewhart’s control charts were introduced in the 1930s and continue to be in wide use today... but there’s a problem. Recall that we used the following as a point estimate for :
This computation exists because it was feasible in the 1930s but it is a biased estimate. It would be great if a more accurate estimate could be made.

## Slide 31: Control Charts - Unbiased
While is an unbiased estimated of , is a biased estimate of
 | Population |  | Sample Data |  |  | St Dev | Var | 
 | 10 |  | A | 10 | 10 | 0 | 0 | 
 | 11 |  | B | 10 | 11 | 0.707107 | 0.5 | 
 | 12 |  | C | 10 | 12 | 1.414214 | 2 | 
Var | 0.666667 |  | D | 11 | 10 | 0.707107 | 0.5 | 
St Dev | 1 |  | E | 11 | 11 | 0 | 0 | 
 |  |  | F | 11 | 12 | 0.707107 | 0.5 | 
 |  |  | G | 12 | 12 | 0 | 0 | 
 |  |  | H | 12 | 10 | 1.414214 | 2 | 
 |  |  | I | 12 | 11 | 0.707107 | 0.5 | 
 |  |  |  |  | Average: | 0.628539 | 0.666667 | 
Here,
But,

## Slide 32: Control Charts – the -Chart obtained using
Introduce a new control chart constant, where,
And we obtain control limits as follows, using an unbiased estimate of process variability

## Slide 33: Control Charts – the -Chart
Effectively, is an unbiased estimate of
Just as we used the -chart previously, we still need a means of identifying when variability within a sample is greater than expected….

## Slide 34: Other Charts

## Slide 35: The -chart
Used for measuring the proportion of defective product. More specifically, for binary response variables, e.g., did the engine start (yes/no)

## Slide 36: The -chart
Used for monitoring the number of defects in a single product/service.

## Slide 37: Coping with Frequency Data

## Slide 38: Frequency Data
Until now, we’ve been working with Ratio data. Sometimes, we have frequencies associated with Categorical (or Nominal) data that isn’t amenable to the type of control charts we’ve seen thus far. For these, we can formulate the problem as a hypothesis test using the chi-squared distribution, where,

## Slide 39: Frequency Data
Conclusion
The defect type is independent from the shift (at the significance level).

## Slide 40: Closing Comments

## Slide 41: Limitations
An in-control process doesn’t imply product is within tolerances or specifications
Control charts are not conclusive evidence for use in RCA
Akin to hypothesis testing,
  Type I Error (α), i.e., false positive
  Type II Error, i.e., false negative
There are many more forms of control charts than what I’ve presented here.

## Slide 42: Case Discussion